## Slide 1
February 2012
Materials for participants of tender for Scoping Study development
Elkon mining and metallurgical plant Development of Yuzhnaya Zone reserves potentially involving Severnoye deposit.
Appendix No. 1. To the Technical Assignment

## Slide 2
JSC «Elkon Mining Metallurgical Plant» is a 100% subsidiary of JSC «Atomredmetzoloto» Uranium Holding (100% of shares belong to RF State Corp. ROSATOM) created in 2007 with the purpose of mining uranium deposits of the Elkon ore field, which is the largest in the world (342 thousand t of uranium or 6% of recoverable world reserves). The ores contain gold, silver and molybdenum as well.
«Elkon MMP» construction project is supported by the governmental program. «Elkon MMP» construction is provided in terms of the “Southern Yakutia integrated development” project, aimed at creation of a new industrial district in Yakutia, involving hydropower industry facilities, power supply network and transport infrastructure.
In terms of public-private partnership JSC «Elkon MMP» carries out geological survey, scientific research and collects the required basic data for Trade-off Study, Scoping Study according to the international standards.
Uranium is contained in a refractory mineral, brannerite, and a finely divided gold is enclosed in pyrite. Enclosing rocks are characterized by a high content of acid-bearing minerals, carbonates and chlorites, in particular.
Design, construction and operation of the enterprise will be performed in full compliance with international standards and current environmental and labour safety legislative norms.
  Introduction

## Slide 3
Elkon Uranium Ore District
Prospected geological reserves of uranium at the Elkon Uranium Ore District comprise 342 thou. t with the ore content of 0.147%
Geological resources of Yuzhnaya Zone comprise 229,834 t of uranium ore at 0.143% content (JORC)
General information | 
Elkon Uranium Ore District | 
Geological reserves of uranium (B+C1+C2) | 342 thou. t
Geological reserves of gold | 191 t
Elkon Project | 
Geological reserves of uranium (B+C1+C2) | 319 thou. t
Geological reserves of gold | 170 t
Yuzhnaya Zone (top-priority project ) | 
Geological resources of uranium (Measured, Indicated, Inferred) | 230 thou. t
Geological resources of gold | 89 t
Recoverable resources of the Elkon Uranium Ore District reach 5.6% of the world reserves
Chart: 
| Россия | Прочие страны | Элькон | Другие
 | 5740 | 309.9 | 256.4
Reserves
of the Elkon MMP
  Elkon project role in uranium reserves of the world
Interesnaya Zone
Elkon
Severnoye
Druzhnoye
Neprokhodimoye
Elkon plateau
Kurung
Lunnoye
1 – Mesozoic intrusions; 2 – platform carbon-bearing Cambrian bodies; 3 – metamorphits and granitoids; 4 – blastomylonites; 5 – revived ancient splits; 6 – Mesozoic tectonic zones; 7 – uranium deposits

## Slide 4
The nearest settlement is Tommot city, where 8,7thou. people live. A branch railway line connects Tommot, Baikal-Amur Mainline and Trans-Siberian Railway. Automobile road and a power supply line lay 10 km to the north of the deposit.
From the history of deposit development:
  Deposit discovery: 1960
  Geological prospecting and exploration: 1960–1980
  Elkon Uranium Ore District

## Slide 5
Elkon
Elkon
plateau
Kurung
Neprokhodimoye
Druzhnoye
Yuzhnaya Zone is a steeply dipping narrow (first metres) ore zone, 20 km long
  Geological map of Yuzhnaya Zone
Yuzhnaya Zone as an uranium-bearing body is developed along the large Southern split formed in Archean-Proterozoic era, regularly renovated in the later periods of tectono-magmatic activity. Yuzhnaya Zone is a convex arc, stretching in the north-west direction from 290° to 315° (305° on average) at the plan, zone is declined to the south-west at an angle of 55–80°.
Zone is traced for a 37 km distance by means of geological and geophysical methods. In the central part of Zone, which is 20.7 km long, in terms of maximum exploration degree and ore content the following deposits are distinguished: Elkon, Elkon plateau, Kurung, Neprokhodimoye and Druzhnoye.

## Slide 6
Deposit | Category of geological reserves (SRC), resources (JORC) |  | Ore reserves in blocks, thou. t | Uranium |  | Gold |  | Silver |  | Molybdenum | 
 |  |  |  | aver. grade, % | reserves, t | aver. grade, g/t | reserves, kg | aver. grade, g/t | reserves, t | aver. grade, % | reserves, t
Yuzhnaya Zone |  |  |  |  |  |  |  |  |  |  | 
Elkon | SRC-1981 (C1+C2)* |  | 11,194 | 0.196 | 21,958 | 0.74 | 8318 | 12.19 | 136.4 |  | 
 | Resources JORC-2010** |  | 21,084 | 0.143 | 30,176 | 0.48 | 10,024 | 4.30 | 90.6 |  | 
Elkon Plateau | SRC-1981 (В+C1+C2) |  | 41,666 | 0.154 | 64,285 | 0.79 | 33,039 | 11.00 | 457.1 |  | 
 | Resources JORC-2010 |  | 50,487 | 0.142 | 71,492 | 0.54 | 27,274 | 7.20 | 362.5 |  | 
Kurung | SRC-1981 (В+C1+C2) |  | 34,584 | 0.159 | 54,849 | 1.00 | 33,039 | 13.22 | 457.1 |  | 
 | JORC-2010 |  | 31,710 | 0.140 | 44,370 | 0.67 | 21,154 | 9.19 | 291.5 |  | 
Neprokhodimoye | SRC-1981 (C2) |  | 18,079 | 0.119 | 21,486 | 1.40 | 26,288 | 7.00 | 127.0 |  | 
 | Resources JORC-2010 |  | 10,404 | 0.132 | 13,737 | 0.79 | 8186 | 7.31 | 76.011 |  | 
Druzhnoye | SRC (C1+C2) |  | 71,188 | 0.134 | 95,238 | 0.60 | 42,833 | 8.53 | 607.1 | 0.076 | 41,632
 | Resources JORC-2010 |  | 47,162 | 0.149 | 70,055 | 0.48 | 22,640 | 5.36 | 252.8 | 0.028 | 13,178
Yuzhnaya Zone, total by categories | SRC-1981 (В) |  | 5181 | 0.167 | 8672 |  |  |  |  |  | 
 | Resources JORC Measured |  | 16,504 | 0.136 | 22,516 | 0.72 | 11,947 | 8.86 | 146 | 0.028 | 205
 | SRC-1981 (C1) |  | 38,438 | 0.142 | 54,783 | 0.86 | 33,052 | 12.16 | 467.4 | 0.052 | 7049
 | Resources JORC Indicated |  | 38,111 | 0.128 | 48,822 | 0.50 | 19,100 | 6.08 | 231.8 | 0.032 | 2500
 | SRC-1981 (C2) |  | 133,092 | 0.146 | 194,361 | 0.81 | 107,977 | 9.90 | 1316.6 | 0.083 | 34,583
 | Resources JORC Inferred |  | 106,232 | 0.149 | 158,496 | 0.55 | 58,231 | 6.54 | 695.3 | 0.028 | 10,473
Yuzhnaya Zone, total | SRC-1981 (В+C1+C2) |  | 176,711 | 0.146 | 257,816 | 0.80 | 141,029 | 10.10 | 1784.0 | 0.076 | 41,632
 | Resources JORC-2010 (Cut off U–0.08%) |  | 160,837 | 0.143 | 229,834 | 0.56 | 89,278 | 6.67 | 1073.4 | 0.028 | 13,178
Severnaya Zone |  |  |  |  |  |  |  |  |  |  | 
Severnoye | C2*** |  | 39,272 | 0.149 | 58,566 | 0.70 | 29,220 | 12.40 | 485.5 |  | 
 | Resources JORC-2011 *** (indicated and inferred) (Cut off U– 0.08%) |  | 55,102 | 0.173 | 95,380 | 0.39 | 21,721 | 7.43 | 409.5 |  | 
Interesnaya Zone |  |  |  |  |  |  |  |  |  |  | 
Interesnaya Zone |  | SRC-1968 (В+C1+C2)**** | 795 | 0.354 | 2814 | 0.40 | 320 |  |  |  | 
Elkon Uranium Ore District, total |  |  | 216,778 | 0.147 | 319,186 | 0.78 | 170,244 | 10.47 | 2269.5 | 0.076 | 41,632
* reserves were approved by SRC in 1981, they are registered in the State Register of Reserves; according to SRC requirements reserves are submitted to reestimation and reconfirmation ** resources estimated in compliance with JORC standards in terms of preparation of Feasibility Study (FS) for reserves exploratory estimation, June 2010 *** follow-up estimate in 1986, reserves were not approved, but they are registered in the State Register of Reserves, *** resources estimated in terms of the block model creation **** reserves approved by SRC in 1968, they are registered in the State Register of Reserves; according to SRC requirements they are submitted to reestimation and reconfirmation
  A summary table of geological reserves (SRC) and resources (JORC)
  of uranium and associated components
  of the Elkon ore cluster deposits

## Slide 7
Average content of chemical components, С > 1%
Average content of chemical components, С < 1%
Chart: 
| SiO2 | Al2O3 | K2O | CO2 | CaO | Fe2O3 | Sобщ. | MgO | Na2O
 | 58 | 12 | 7.2 | 4.9 | 4.6 | 3.9 | 2.2 | 1.7 | 1.5
Chart: 
| Sсульф. | FeO | TiO2 | P2O5 | U | V2O5 | MnO
 | 0.92056 | 0.84 | 0.8 | 0.5 | 0.11 | 0.069444 | 0.043667
Chart: 
| Au | Ag
 | 0.8 | 5.8
Average content of the associated components
On Druzhnoye deposit
Мо (Cav-0.085%) is an associated valuable component
Uranium minerals are represented by
brannerite, titaniumsilicates and uranium oxides with negligible amount of coffinite and uranium-enclosing leucoxene
Mineral composition of ore-bearing metasomatites
Potassium feldspar (microcline, orthoclase) — 35–40%
sodium-calcium feldspar (oligoclase, albite) — 10–15%
quartz — 30–35%
carbonates (ferrodolomite, calcite) — 6–11%
micas (muscovite, sericite) — 3–4%
ore minerals (pyrite, marcasite, uranium minerals) — 2–3%
accessory minerals — apatite, zircon, octahedrite, rutile, sphen
pelitic substance – 1–2%
Complex gold and uranium ores of Yuzhnaya Zone deposits refer to one type of processing, particularly, refractory aluminosilicate ores
  Composition and processing behaviour of ores

## Slide 8
  Production zone of the Southern split complex system is a flattened linear uranium ore stockwork which coincides with the border of the pre-ore pyrite-carbonate- potassium-feldspar metasomatosis volumetric manifestation by the outer contour in a first approximation. Its thickness varies from 10 to 30 m, and horizontal extension is defined by the length of Yuzhnaya Zone split ore-bearing area, i.e. 20.7 km. Vertically mineralization is spreading over 2 km.
  Ore lodes at the deposit correspond to the systems of tectonic wedges, which control the ore bodies. Horizontally ore lodes stretch up to several kilometers, and vertically – up to hundreds of meters.
  Ore bodies are independent uranium ore blocks, confined to individual tectonic wedges or a series of contiguous fractures and outlined according to the specified standard requirements. Horizontal extension of ore bodies at the deposit varies from 20–30 to 650–700 m at a thickness from tens of centimeters to 2–5 meters. Vertical extension of ore bodies usually is less in comparison with the horizontal one and it comprises 200–350 m. Maximum size down the plunge of ore bodies is up to 800–1000 m.
  Ore bodies can be distinguished only on gallery levels and in raises, that is over a dense survey grid.
  Production zone
  Ore lodes
  Ore bodies
  Interpretation of ore bodies and lodes of Yuzhnaya Zone, and of extended ore channels as well, which was approved after the estimate in 1980, does not correspond to the deposit geology. The more careful approach would be a presentation of the deposit in a form of a flattened stockwork, which complies with the FS requirements dated 1977. Factually, the ore-bearing zone refers to the II category of complexity, and uranium inner distribution over it corresponds to III–IV categories of complexity. As a consequence, wire-frame 3D modelling at the agreed exploration grid turned possible only at 0.01% cut-off grade of uranium, and classification of internal ore zone structure required application of specific approaches.
  Geological and mathematical model building Geological peculiarities of Yuzhnaya Zone deposits

## Slide 9: Detailed project working scheme
Construction
U production
Restoration
Selection of the key versions
of the project implementation.
Decision on the careful
study of existing versions
of the project implementation.
Choosing the best solution. Decision on the detailed study of the given version of the project implementation
(Decision on the beginning of the study
of design documentation FS).
Considering the results of the Scoping Study.
Decision on the enterprise putting into operation.
Decision on participating
in the project.
Decision on performance
of the preliminary
Survey.
Decision on the enterprise decomissioning.
Decision on the project closure.
А
1.0
А
2.0
В1.1
В2
С1
Investment phase
А1
Making decision on the project suspension. Scoping Study development.
2007
Exploration and reserves estimation of Yuzhnaya Zone
Project management
Decision on the enterprise construction.
Choosing the best version of the project implementation. Decision on the detailed study of this version.
А2
В1
В3
С2
2008
2009
2010
2011
2012
2013
2014
2015
2016
2017
2018
2019
2020
2021
2022
2023
2024
2025
JOI
Designing
Designing and State Expertise
SS
PFS
Cashcall, license application
ТО PFS
FS
2025-ХХХХ
ХХХХ+2
ХХХХ+1
Exploration and reserves estimation of Severnoye deposit
Pre-investment phase
Post-investment phase
2006
Stage 3.
FS
Stage 4.
Design and construction
Stage 5.
Operation
Stage 6.
Restoration
Pre-conception
Scoping Study
PFS
FS
Designing and Construction
Operation
Site restoration
PFS
SS
Stage 2.
JOI
Stage2.1.
Concept
Stage 2.2
JOI
PCN
Feasibility Report
Feasibility Study and Proposals
Construction
Ore mining
Stage 0.
Preliminary concept
Stage 1.
Concept
9
Decision on designing renewal after SS or after PFS

## Slide 10
Pre-concept
PFS
JOI
Designing
Positive project economics is proved by the technical and economic estimate of the VNIPIPT
An application to the Investment Fund of the Russian Federation is prepared
Exploration of Yuzhnaya Zone
2008
2009
2010
Promotion of the application for cash receipt from the Investment Fund of the Russian Federation
Design passport of the “Southern Yakutia integrated development” project is approved
The I tranche from the IF of the RF is received
Completion of JOI development
A trial of the project optimization on the basis of best practice
Technical and economic estimate
Reserves estimate, FS
Reasons for the Scoping Study development
In the course of JOI development OSC “VNIPIpromtechnologii” a non-optimum opening scheme for Yuzhnaya Zone deposits was accepted (with two cascades, 13 vertical shafts, a skip hoisting and railway line on the surface) and other technical solutions, which became an obstacle to getting a feasible design solution.
In 2010–2011 the Hatch company prepared PFS proceeding from the JOI materials. In this case the result was greatly influenced by the following factors:
      The mining model was created via the MSO Datamain with a standard fixed size mining block. As a result the reserves in the ore bodies less than 1 m thickness have been eliminated for further evaluation. Isolated and losted reserves were also excluded. So, total rest reserves (down to the level -700 m) were 61,606 thousand tons of ore and 83,341 tons of uranium.
      It was necessary to agree all solutions with OSC "VNIPIpromtekhnologii."
In terms of the current restrictions a trial of the project optimization did not succeed.
2011
2012
Optimization of the technical solutions, included into JOI and the project
Scoping
Study
Trade-off Study
Designing
Project history

## Slide 11
Pre-concept
PFS
JOI
Designing
Positive project economics is proved by the technical and economic estimate of the VNIPIPT
An application to the Investment Fund of the Russian Federation is prepared
Exploration of Yuzhnaya Zone
2008
2009
2010
Promotion of the application for cash receipt from the Investment Fund of the Russian Federation
Design passport of the “Southern Yakutia integrated development” project is approved
The I tranche from the IF of the RF is received
Completion of JOI development
A trial of the project optimization on the basis of best practice
Technical and economic estimate
Reserves estimate, FS
Reasons for the Scoping Study development
FS of of geological conditions was considerably revised:
  It was kept a large part of reserves in the ore bodies with thickness of 1 m or less owing to use the delineation of ore bodies of the elementary counted block. Operational reserves were increased up to 177,444 thous. tons of ore and 205,732 tons of uranium.
  Opening scheme of mine involving 4 vertical shafts, 2 inclined shafts and a belt conveyor for rock hoisting to the ore processing complex were developed.
Development time restrictions (to the end of 2011) prevented the entire optimization of the project, but allowed to raise its feasibility considerably.
In order to study thoroughly all versions of the project development in new conditions due to the well-known events in Japan, a decision on the Scoping Study development was taken, involving review of the project concept and maximum application of advanced technical solutions.
A number of the Trade-off Studies were developed as a first stage of the Scoping Study, their results and the Initial Data for the Scoping Study development would be given to the Contractor.
2011
2012
Optimization of the technical solutions, included into JOI and the project
Scoping
Study
Trade-off Study
Designing
Project history

## Slide 12
  R&D and Trade-off Study are performed, providing initial data for the further design of the Elkon MMP based on the estimate of alternative versions of the deposit development.
  For performance of these works a number of Russian (SPb-Giproshakht, RUSBURMASH and other) and foreign (CSA Global, MiningPlus, FLSmidth, Hatch, WorleyParsons and other) consulting and engineering companies were engaged.
  Intermediate results received in the course of R&D and Trade-off Study development are supposed to provide an opportunity at the turn of 2011–2012 to prepare a Scoping Study and consider a version of gradual development of the deposit, which provides for speeding up facilities commissioning and the higher technical and economical project indicators. Herewith, along with the optimization of project indicators the preparation of design documentation for the first stage of deposit development is supposed to speed up.
2011
2012
3 quarter
4 quarter
1 quarter
2 quarter
3 quarter
4 quarter
R&D
Trade-off Studies development
Scoping Study development
Optimization
Design
Design
Decisions on optimization
  Current operations

## Slide 13
13
1.
Estimate and confirmation of reserves
2.
Design documentation development
3.
Support of the project on investor attraction
Estimate and confirmation of reserves
Electronic databases of Yuzhnaya Zone and Severnoye deposits are prepared
Geological survey operations are performed at the Elkon Uranium Ore District: Elkon, Neprokhodimoye, Druzhnoye, Severnoye (in total, 100,806.1 m of boreholes were drilled)
Geological and mathematical (block) models of Yuzhnaya Zone and Severnoye deposit are developed, the estimate of resources according to JORC standard is done
On Yuzhnaya Zone deposits a report on resources and reserves is prepared in compliance with JORC standard
FS of requirements for Yuzhnaya Zone deposits is prepared and presented to the State Committee of Geological Reserves (GKZ).
Development of design estimate documentation
R&D
Semi-industrial testing have been performed for the sample of 50 t
Semi-industrial testing of the processing technology providing continuous atmospheric sulphuric-acid ore leaching in the pilot hydrometallurgical shop for the sample of 500 tons
- A technical procedure for ore processing is developed
- Process regulations are prepared
- R&D program for SS is fulfilled
Engineering survey
Engineering and geological survey for the plant construction objects have been carried out/
Support of the project on investor attraction
The PFS Technical Report and the Report on Investment Decision Making are developed
A visit of Japanese delegation to the deposits and the plant construction site is arranged
Activities performance in terms of the project implementation in 2011

## Slide 14
In 2011 opportunities for entry of the high-cost projects into the market were reduced because of Fukusima NPP failure, which resulted into reduction of the uranium price by 30%
Chart: 
| 01/17/2011 | 01/24/2011 | 01/31/2011 | 02/14/2011 | 02/21/2011 | 02/28/2011 | 03/14/2011 | 03/21/2011 | 03/28/2011 | 04/18/2011 | 04/25/2011 | 05/16/2011 | 05/30/2011 | 06/13/2011 | 06/20/2011 | 06/27/2011 | 07/18/2011 | 07/25/2011 | 08/15/2011 | 08/22/2011 | 08/30/2011
Цена U3O8, долл/фунт | 68 | 70 | 73 | 72.25 | 68.75 | 69.75 | 60 | 60 | 62.5 | 57.25 | 55.5 | 57.75 | 57.5 | 54.75 | 54.5 | 54.25 | 53.5 | 51.5 | 50.5 | 50.5 | 48.85
-30%
U3O8 price movement in 2011, USD/GBP
For project implementation in the changed conditions the project is being optimized at a present moment: development of R&D, Trade-off Studies, Scoping Study, optimization of technical solutions (optimization of the enterprise commissioning schedule, mining technical solutions, processing procedure).
  Influence of Fukusima NPP failure on the project
14
Reduction of NPP capacity in the world in 2011, GW
Before March 2011
After March 2011
Shut off because of Fukusima failure
Temporarily stopped because of Fukusima failure
In operation

## Slide 15
  Optimization of the opening scheme
  and mining sequence of the deposits
The former version of the opening scheme
12 vertical shafts mining scheme
(JOI, PFS Technical Report)
Mining scheme providing 4 vertical shafts and 2 slopes
(FS of the requirements, Trade-off Study of the effective annual mining production verification.)
pillar
Belt slope
Auxiliary slope
Unified mine
Elkon district
Elkon plateau district
Kurung district
Neprokhodimiy district
Elkon mine
Shaft No. 1
Shaft No. 2
Shaft No. 3
Shaft No. 4
Kurung mine
Neprokhodimiy mine
Mine 1
Mine 2
Mine 3
Mine 1
Shaft 1
Shaft 2
Shaft 3
Shaft 4
Shaft 5
Shaft 6
Shaft 7
Shaft 9
Shaft 8
Shaft 11
Shaft 13
Shaft 12
Inter-cascade

## Slide 16
In order to reduce costs for rock mass transportation from the mine to the ore-processing complex (OPC), according to FS the latter is shifted 4 km closer to the deposit, the belt slope will be used for ore transportation rising near the OPC, equipped with the conveyor belt METSO, which is characterized by the annual production of up to 7 mln. t.
  Movement the ore-processing complex closer to the deposit and application of the belt slope
The former OPC
Belt slope
OPC
location
route

## Slide 17: Horizon-chamber mining system with sublevel stoping and bottom ore collection
Producing block sizes from 100 х 60 m to 300 х 60 m
Producing block output comprises 1 mln. t/year and above
LHD technique and remote control are used
Ore is loaded at the ore-tramming floor only
Common preparation method allows application of any mining system depending on the mining and geological conditions
Driving sublevel entries and workings of the block bottom, boreholes drilling at the sublevels, blasting
Output of broken ore from shrink stopes, rock mass delivery through the orts, the crosscuts in the block bottom
Filling extracted chambers with stowing based on the OPC tails, rock mass after XRS
Research: FS of main solutions on mining systems selection and statement of the producing block standard output, mining technique feasibility, reserves mining sequence and the opening scheme
100 m
60 m

## Slide 18
  Innovation tendencies of
  technical solutions optimization
Application of the belt conveyor 11.5 km long instead of a railway line for ore delivery to OPC
Innovation tendency
Expected effect
Capital costs
Operating costs
Environmental impact
Paste filling application
Reduction of capital costs for a tailing dump
Reduction of tails transportation and solid stowing costs due to application of the efficient composition
Reduction of tails environmental impact
Development of the efficient opening scheme, involving 4 vertical shafts and 2 inclined shafts
Reduction of capital costs for main openings, equipment and surface facilities
Reduction of surface facilities, ore and rock storehouses.
OPC shift to the Yuzhnaya Zone and Severnoye deposits
by 4 km
Shift of treatment facilities closer to the ore-processing complex
Application of Metso Minerals belt conveyor
Construction of the railway section was cancelled
Reduction of transportation costs
Reduction of the environmental impact due to the close scheme application
Application of paste filling reduces the tailings dam size approx. two times
Production panels efficiency optimization
Panel production growth by 2 times and above due to transition to the vertical chamber mining system and production modules
Mining concentration, reduction of radon release into the air
Reduction of the capital costs for the surface gallery construction, ore re-loading unit and OPC storage facilities
Reduction of operating costs on the account of reduction the ore transportation distance by the inclined shafts , 25%.
Raising up the panel efficiency, refusal from the second mining cascade construction aimed at costs reduction
Reduction of operating costs due to the use of the efficient transportation routes over the inclined shafts by 25%.
Vent (air relief) shaft
Air supplying shaft
Conveyor inclined shaft
Inclined shaft for the large-size equipment going
Horizon
Concentration shaft
S=18,6 m
S=18,9 m
Shaft 1
Shaft 4
Shaft 2
Shaft 3

## Slide 19: Ore-processing complex procedure
Uranium recovery – 91%
Final product is uranium chemical concentrate
Acc. to ASTM C967-08 instead of
uranium oxide concentrate acc. to TU 95-2009
Gold recovery ~ 40%, silver ~ 25%, molybdenum – 36%
Advantages
  Minimum equipment amount
  Streamlined technological procedure (excluding extraction)
  Minimum capital and operating costs
pressure leaching
sand-slime separation
U sorption
desorption
precipitation,
filtration, drying
yellow cake acc. to ASTM C967-08
flotation
cyanide leaching
Uranium recovery – 96%
Uranium recovery – 96.4%
t = 140°C
P = 15 atm
T = 4 hours
Sulphuric acid – 14%
Diluted uranium – 10–12 g/l

## Slide 20: Summary
This presentation complements the Technical Assignment for Scoping Study and comments:
  The main characteristics of deposits of Elkon uranium ore district.
  The milestones of the project and the current situation.
  The key results of completed work to the date, which will be transmitted to the Contractor as an Initial Data (a list of work attached to the Technical Assignment for the Scoping Study development).

## Slide 21: Contact list
Officer in charge of project:
  Adviser of General Director of JSC «Atomredmetzoloto»
  Leskov Mikhail Ivanovich:
    E-mail: leskov.m.i@armz.ru
    Phone: (7 495) 508-88-08
Project manager:
  General Director of CJSC « Elkon mining metallurgical plant»
  Varvara Oleg Vladimirovich:
    E-mail: varvara.o.v@armz.ru
    Phone: (7 495) 644-35-36
Executive manager:
  Executive manager of CJSC « Elkon mining metallurgical plant»
  Sotsilenkov Dmitriy Aleksandrovich
    E-mail: sotsilenkov.d.a@armz.ru
    Phone: (7 495) 644-35-36
Expert in purchases:
  Expert of Purchases Department of JSC «Atomredmetzoloto»
  Zaytsev Aleksey Pavlovich
    E-mail: zaytsev.a.p@armz.ru
    Phone: (7 495) 508-88-08